## Slide 1
Prof. Sbarufatti Claudio Eng. Poloni Dario
A.Y. 2021-22
Group 02
NUCLEAR MARINE PROPULSION FLEET
Sophie Deanesi | 10607418
Davide Fracasso | 10567984
Zeno Mancassola | 10607116
Paolo Pontillo | 10565989
Davide Portello | 10624353
DIGITAL TWIN FOR ENERGY SYSTEM MANAGMENT

## Slide 2: The problem
NUCLEAR MARINE PROPULSION FLEET
THE PROBLEM
POSSIBLE SHIP DAMAGES
MANAGEMENT
Degradation of admission valve of the turbine
Damage on bearing of the generator shaft
Crack propagation on the pressure vessel
Flow management
Maintenance operations
Personnel and material management
Cost analysis
Problem  Propulsion Model  Damages  Port model  Results
1

## Slide 3: The Model
NAVAL PROPULSION REACTOR
~ 30 – 300 MWth
Fuel enrichment
U-TUBE STEAM GENERATOR
NUCLEAR REACTOR
TURBINE
CONDENSER
PUMP
T_in
NUCLEAR REACTOR
AP600 PWR Westinghouse (1940 MWth)
T_in = 299.74 [°C]
Problem  Propulsion Model  Damages  Port model  Results
2

## Slide 4: Simscape components
BOILER
Coupling between reactor and secondary side
Convective thermal resistance
Input: fluid from pump
Output : saturated steam to the turbine
Ouput : liquid volume fraction to PI controller
Problem  Propulsion Model  Damages  Port model  Results
3

## Slide 5: Simscape components
THROTTLE VALVE
Model of a pressure drop
Output : Admission steam to turbine
AR/Throttle imposed by PI controller
TURBINE
Inlet and outlet port for the fluid
Mechanical rotational conserving ports
Ideal torque sensor & Ideal angular velocity source
Output power to the PI controller
Problem  Propulsion Model  Damages  Port model  Results
4

## Slide 6: Simscape components
Problem  Propulsion Model  Damages  Port model  Results
CONDENSER
Saturated Fluid Chamber
Input : fluid from Turbine
Output : fluid to the pump
Output : liquid level
Sea Temperature = 15 [°C]
PUMP
IDEAL mechanical energy source
Input : saturated liquid from condenser
Input : mass flowrate from PI controller
5

## Slide 7: Simscape components
PI CONTROLLERS
Restriction area of the control Valve regulation to satisfy power demand
(2) Mass flowrate to the pump regulation according to the liquid level in the boiler
SENSORS
- Sensors chosen according to damage (to be continued…)
Problem  Propulsion Model  Damages  Port model  Results
6

## Slide 8: Rankine cycle
x = 73.79 %
mdot_nominal = 41.022 [kg/s]
input thermal power = 100 [MWth]
Problem  Propulsion Model  Damages  Port model  Results
7

## Slide 9: Maintenance operations: the port model
Failure repair  Maintenance area operations
Port flow mapping:
  Maintenance areas
  Warehouses
  Waiting area
  Load/unload areas
  Workers behaviour
Performance analysis
Cost analysis
Problem  Propulsion Model  Damages  Port model  Results

## Slide 10: Damage 1: Valve
CORROSION & MATERIAL DEPOSITION
± 30 % nominal valve passage area
NOMINAL CONDITION
Power demand = 25 [MW]
Throttle = 0.009 [m2]
SENSORS
Pressure sensor at the outlet of the valve
Power sensor output of the turbine
NO detection of differences
PI controller regulation
CORROSION
CORROSION & FOULING
Problem  Propulsion Model  Damages  Port model  Results
8

## Slide 11: Damage 1: Valve 1ST MODEL
ANN
Two saparate ANN for power and pressure
Input : valve passage area
Output : mean of last 100 second measurements
Sweep from 0.009 to 0.0117 m2 (severe damage : +30% nominal value)
nftool
PERFORMANCE ASSESSMENT
areaValve= 0.01102 m2
1ST MODEL
PI CONTROLLER
CORROSION ONLY
Problem  Propulsion Model  Damages  Port model  Results
9

## Slide 12: Damage 1: Valve 1ST MODEL
MCMC
Virtual experimental dataset, 100 noise samples
Gaussian noise : [MW] [MPa]
areaValve= 0.00973 [m2] (true value)
Uniform prior
Starting point 0.01 [m2]
Gaussian transition function
Chain length = 10000
Problem  Propulsion Model  Damages  Port model  Results
10

## Slide 13: Damage 1: Valve 1ST MODEL
RUL
Threshold valva passage area +10 % nominal value
[m2]
Constant homogenous thinning rate
Problem  Propulsion Model  Damages  Port model  Results
11

## Slide 14: Damage 1: Valve 1ST MODEL
ANOMALY DETECTION
200 Gaussian noise samples : 100 to evaluate standard deviation, 100 samples to build z-score
Threshold 5% probability of false alarms
Damage dataset : ANN dataset corrupted by noise
Problem  Propulsion Model  Damages  Port model  Results
12

## Slide 15: Damage 1: Valve 2ND MODEL
ANN
Sweep from 0.0063 to 0.0117 m2 (severe damage : ±30% nominal value)
PERFORMANCE ASSESSMENT areaValve= 0.01102 m2
2ND MODEL
NO PI CONTROLLER
CORROSION & FOULING
Problem  Propulsion Model  Damages  Port model  Results
13

## Slide 16: Damage 1: Valve 2ND MODEL
MCMC
areaValve= 0.00813 [m2] (true value)
Problem  Propulsion Model  Damages  Port model  Results
14

## Slide 17: Damage 1: Valve 2ND MODEL
RUL [m2] -10 % nominal value
Problem  Propulsion Model  Damages  Port model  Results
15

## Slide 18: Damage 1: Valve 2ND MODEL
ANOMALY DETECTION
Problem  Propulsion Model  Damages  Port model  Results
16

## Slide 19: Damage 2: Bearing
One of the bearings supporting the electric generator shaft is subjected to pitting.
Pitting occurring on the inner race of the bearing is considered: this phenomenon causes an impulsive decrease of bearing stiffness with frequency:
The force acting on the bearing is due to load imbalance of the rotor and it’s synchronous with the shaft rotation.
Problem  Propulsion Model  Damages  Port model  Results
17

## Slide 20: Damage 2: Bearing
Starting from the nominal stiffness of the bearing (1e7 N/m), this value is decreased by a quantity Δk that depends on the depth of the damage according to a formula that interpolates the following values:
With no defect, Δk is equal to 0
With 0.1 mm deep pit, Δk is equal to 8e4 N/m
With 1 mm deep pit (limit value), Δk is equal to 9e6 N/m.
Problem  Propulsion Model  Damages  Port model  Results
18

## Slide 21: Damage 2: Bearing
Fourier transform of the acquired signal (with pit depth 0.4 mm) yields this spectrum. Components centered at frequencies around BPFI arise. However, it’s difficult to evaluate health basing on the spectrum of the signal.
Time domain analysis allows to compute the Crest Factor, that is an indicator of impulsive peaks of vibrations. It’s more efficient than RMS.
FREQUENCY AND TIME ANALYSIS
Problem  Propulsion Model  Damages  Port model  Results
19

## Slide 22: Damage 2: Bearing
An ANN is trained for a pit depth between 0.1 mm and 1 mm. Output of the ANN is the CF.
Then, MCMC for the evaluation of the pit depth was built. The prior distribution is an uniform distribution between 0 and 1 mm depth; the transition distribution is normal with properly tuned variance. The generated MCMC approaches well the real value of the parameter.
ANN AND MCMC
Problem  Propulsion Model  Damages  Port model  Results
20

## Slide 23: Damage 2: Bearing
First the model is run in undamaged condition. Z-score with respect to Crest Factor is computed and limits for anomaly detection are determined at mean(z-score) ± 2std(z-score).
Then the model is run with pit depth varying from minimum to maximum value and z-scores are computed: damage starts to be detected from 0.3 mm deep pit.
ANOMALY DETECTION
Problem  Propulsion Model  Damages  Port model  Results
21

## Slide 24: Damage 2: Bearing
Material: steel 42CrMo4
Pit (crack) development:
Crack driver: contact stress between roller and cage with BPFI cycles/s
When pit is 0.3 mm deep, RUL is about 190 days
RUL ESTIMATION
Threshold 0.8 mm for safety
Nominal guaranteed life:
that yields 15 years
Problem  Propulsion Model  Damages  Port model  Results
22

## Slide 25: Damage 3: Crack propagation due to pressure fluctuation
Variation in the power demand
Power control obtained using a throttle valve
Throttle valve increases the pressure inside the reactor pressure vessel (RPV)
PHENOMENON OF PRESSURE FLUCTUATION
Problem  Propulsion Model  Damages  Port model  Results
23

## Slide 26: Damage 3: Crack propagation due to pressure fluctuation
RPV material 22NiMoCr37
 | YS [MPa] | UTS [MPa] | KI [MPa] | C [mm/cycle] | m | γ
22NiMoCr37 | 800 | 485 | 160 | 4.0310-9 | 3.08 | 0.42
 | YS [MPa] | UTS [MPa] |  | C [mm/cycle] | m | γ
22NiMoCr37 | 800 | 485 | 160 |  | 3.08 | 0.42
CHARACTERISTICS OF THE RPV
Problem  Propulsion Model  Damages  Port model  Results
24

## Slide 27: Damage 3: Crack propagation due to pressure fluctuation
STRESS DISTRIBUTION
 | Axial [MPa] | Hoop [MPa] | Radial [MPa]
Mean | 31.6570 | 70.0642 | -6.7503
Alternate | 2.8590 | 6.3275 | -0.6096
σaxial nominal = 28.7980 MPa
σaxial reduced = 34.5159 MPa
σhoop nominal = 63.7367 MPa
σhoop reduced = 76.3917 MPa
σradial nominal = -6.1407 MPa
σradial reduced = -7.3599 MPa
Problem  Propulsion Model  Damages  Port model  Results
25

## Slide 28: Damage 3: Crack propagation due to pressure fluctuation
RESISTANCE ASSESMENT
- Static assesment
- Fatigue assesment
Problem  Propulsion Model  Damages  Port model  Results
26

## Slide 29: Damage 3: Crack propagation due to pressure fluctuation
CRITICAL CRACK CALCULATIONS
A semicircular crack was considered
θ = 90°
β = 0.65253527
Critical crack length
acritical plastic = 6605 mm
acritical brittle = 658.23 mm
If a failure occurs it will be a brittle failure
RPV is a critical component
Therfore a conservative critical crack length dimension is 117.5 mm
Problem  Propulsion Model  Damages  Port model  Results
27

## Slide 30: Damage 3: Crack propagation due to pressure fluctuation
Dataset
Particle filter estimation
RUL
RUL in cycles: 3381 cycles
RUL in days: 1127 days
RUL in years: 3 years
Please note that the crack propagates from a 30 mm initial crack length
Problem  Propulsion Model  Damages  Port model  Results
28

## Slide 31: Maintenance activity: the reference framework
Reference port layout, La Spezia (Italy):
  2 zones: Military area and civil area
  Military area:
    Maintenance operations
    Daily operations piers
  Civil area:
    Daily operations piers (load / unload)
  Shared port entry and port exit
Problem  Propulsion Model  Damages  Port model  Results
29

## Slide 32: Maintenance activity: the problem
SCENARIOS | STANDARD SCENARIO | DIGITAL TWIN SCENARIO
Type of maintenance | Predetermined (time-based) and scheduled | Predictive, based on the RUL calculated with the developed models
Distinctive element | The maximum allowed lifetime of each component of the analysis (pressure vessel, valve, bearing) is the only difference between the two scenarios. It will be integrated in the block called Port entry. | 
Common elements | Every parameter of the analysis is not differential between the two scenarios: working times, number of ships and simulation time are the same. | 
CHARATERISTICS TIMES
MODEL ELEMENTS
PERFORMANCE INDICATORS
COST INDICATORS
Port framework and model elements are necessary to derive:
PERFORMANCE INDICATORS
COST INDICATORS
Indicators  Scenario comparison
OUTPUT  Feasibility in DT adoption
Problem  Propulsion Model  Damages  Port model  Results
30

## Slide 33: Maintenance activity: the general model
Modelled ships:
9 aircraft carriers
9 war submarines
32 commercial boats
Ship launch interval:
80 days
Useful modeled life
14600 days (40 years)
Launch
Undamaged area
Maintenance / Undamaged area
Mission
Military ship lifecycle
Problem  Propulsion Model  Damages  Port model  Results
31

## Slide 34: Maintenance activity: Focus
DT scenario
Max lifespan depend on developed RUL models
Max lifespan is reduced by 234 days (99.7% of mission duration)
Standard scenario
Max lifespan depend on literature data
Entity.Damage attribute is changed
Path is chosen according to IsDamaged attribute
PORT ENTRY
DAMAGE CHECK
PORT EXIT
Paths are aggregated before the physical port exit
Problem  Propulsion Model  Damages  Port model  Results
32

## Slide 35: Maintenance activity: Focus
MAINTENANCE AREA
WAREHOUSES
Initial capacity: 20 repair kits
Replenishment threshold: 2 kits
Maintenance areas and warehouses are specific for each type of failure: 3 repair areas and 3 tool stocks
Entry depends on entity.Damage attribute
4 workers per maintenance area, repair tool is taken from the warehouse
Dedicated waiting area
Process times differs according to different type of vessel / type of damage
Problem  Propulsion Model  Damages  Port model  Results
33

## Slide 36: Maintenance activity: Focus
DAILY OPERATION - MILITARY AREA
DAILY OPERATION – CIVIL AREA
Every commercial boat
Load/unload operations
Not maintenance-linked areas  same port resources  congestion
Undamaged military vessels
Arming the warship/submarine for the next mission
Mean arming time: 6 days
2 dedicated piers
Eventual waiting area
Mean time: 7 hours
3 dedicated piers
Problem  Propulsion Model  Damages  Port model  Results
34

## Slide 37: Maintenance activity: Focus
PERSONNEL MANAGEMENT
MISSION SIMULATOR
5 mission scenarios
Cumulated entity.WorkTime is updated
Military: from 25 to 180 days
Civil: 11 days
Workers pool: 14 operators per each turn
3 turns/day; 7 days/week
Involved in maintenance (4 x 3) and check activities (2)
10%: daily illness probability
Illness days: from 3 to 6
Problem  Propulsion Model  Damages  Port model  Results
35

## Slide 38: Maintenance activity: Performance and cost analysis
CHARATERISTICS TIMES
MODEL ELEMENTS
PERFORMANCE INDICATORS
COST INDICATORS
Lifetime status analysis
Total repair cycles
Maintenance waiting area
Energy, space occupation, machinery utilisation
Worked hours
Kit used
Problem  Propulsion Model  Damages  Port model  Results
36

## Slide 39: Maintenance activity: Total repair cycles
Intra-scenario
Highlight single behaviour variability
SINGLE SHIP REPAIR CYCLES
FLEET AGGREGATED REPAIR CYCLES
-36.3%
-13.4%
-22.6%
-35.6%
-13.0%
-36.9%
DT lower than standard case
Bearing is the least repaired
Submarines lower than warships
Valve repair cycles: lowest benefit
Problem  Propulsion Model  Damages  Port model  Results
37

## Slide 40: Maintenance activity: Total repair cycles
DT scenario  fewer repair cycles  more “useful life”
STD showed similar behaviours
TOTAL MISSION TIMES
FLEET REPAIR CYCLES / MISSION DAY
-41.9%
Higher mission time  higher improvement
10.4%
9.6%
-21.6%
-29.6%
-41.7%
-21.2%
-42.9%
Problem  Propulsion Model  Damages  Port model  Results
38

## Slide 41: Maintenance activity: Total repair cycles
Same trend of repair cycles
TOTAL MAINTENANCE TIMES
GLOBAL RESULT
DT: Higher efficiency  higher productivity
-24.3%
-24.7%
8%
6%
10%
7.5%
71%
78%
66%
73%
Problem  Propulsion Model  Damages  Port model  Results
39

## Slide 42: Maintenance activity: Total repair cycles
Standard case  higher costs + higher variability
Space cost  highest variability for standard case
MATERIAL COSTS
COSTS BY COST INDEX
26.4 M€
73%
SPACE COSTS
EQUIPMENT COSTS
WORKING COSTS
31.9 M€
27.6 M€
8.49 B€
83.7 M€
8.3 M€
10.9 M€
11.1 B€
Problem  Propulsion Model  Damages  Port model  Results
40

## Slide 43: Maintenance activity: Total repair cycles
Lowest improvement Material costs
-17.3%
TOTAL COSTS
COSTS BY COST INDEX
8.6 B€
73%
PERCENTAGE ANALYSIS
11.2 B€
Highest improvement Space costs
-67.3%
Median improvement Space costs
-23.7%
Problem  Propulsion Model  Damages  Port model  Results
41

## Slide 44: Possible improvements
73%
Davide Portello
MSc in Management Engineering
Sophie Deanesi
Zeno Mancassola
Paolo Pontillo
Davide Fracasso
MSc in Management Engineering
MSc in Nuclear Engineering
MSc in Mechanical Engineering
MSc in Mechanical Engineering
Marine steam turbine plant model
Valve damage
Bearing model & damage
Port model
Performance & cost analysis
Port model
Performance & cost analysis
Marine steam turbine plant model
Crack progation
42

## Slide 45
THANK YOU FOR THE ATTENTION